Chapter 3-5 Problem V (+1)				Name _____________________

- Yvette hangs a 2.4 kg bird feeder in the middle of a rope tied between two trees. The feeder creates a tension of 480 N in each side of the rope. A) If the two trees are 4.0 m apart, how much will the rope sag in the center? B) If a bird land on the feeder, will this have any effect on the tension in the rope?

- After pulling his car off the side of the road during a rainstorm, Travis is dismayed to find that the car has become stuck in the mud. Travis ties one end of a rope to the front of the car and the other end to a tree 12.00 m away.  A) If Travis can exert a force of 610 N on the rope, moving it 1.00 m in the direction shown, how much force will the rope exert on the car? B) Why is this method better than simply tying a rope to the front of the car and pulling the car straight out?

- A traffic light weighing 100 N hangs from a cable tied to two other cables fastened to a support as shown. The upper cables make angles of 37( and 53( with the horizontal. Find the tension in each of the three cables.

- A child holds a sled at rest on a friction-less snow-covered hill, as shown. If the sled weighs 100 N, find the force the child must exert on the rope and the force the hill exerts on the sled.

- Find the tension in the two wires that support the 100 N light fixture. Both wires make 40( angle from the horizontal.

Sample Problem:

A 150 N bird feeder is supported by three cables as shown. Find the tension in each cable.